## Slide 1
Quantum-Inspired Cyber Threat Detection
for teleportation-based Quantum Digital Signature systems
Core problem
Classical public-key signatures such as RSA and ECC depend on hardness assumptions that become vulnerable to sufficiently powerful quantum computers. The proposed system replaces that trust model with quantum evidence: unknown qubits cannot be copied perfectly, and unauthorized measurement leaves disturbance that can be verified later.
Project stance: deterministic physics checks only. No AI/ML classifier is required; every decision comes from QBER, mismatch rates, verifier asymmetry, freshness, and authentication fields.
Threats covered
Eavesdropping / tampering
External signature forgery
Dishonest verifier forgery
Repudiation between Bob and Charlie
Replay and sender impersonation
Output: a Qiskit/Aer simulation framework, adversary testbed, deterministic threat engine, security-math module, socket-network demo, and real-time telemetry dashboard.
Quantum Digital Signature (QDS) threat detection
1/5

## Slide 2
QDS mechanism: signature becomes quantum evidence
Alice signs with BB84-style qubit tokens; verifiers store eliminated-state evidence before the classical signature is revealed.
Alice prepares
For message k=0 and k=1, Alice creates n entries: (bit, basis). Each entry maps to |0>, |1>, |+>, or |->.
>
Distribute tokens
Quantum signature tokens are sent to Bob and Charlie over a channel that can include noise or Eve.
>
Symmetrise
Bob and Charlie randomly Keep (K) or Forward (F), so Alice cannot predict which verifier holds which evidence.
>
State elimination
Measurements do not need to identify the exact state; they record one or two impossible states per position.
>
Reveal & verify
Alice reveals the classical (bit, basis) list. Any claimed state found in a verifier eliminated-state table is a contradiction.
BB84 token map
Bit
Basis
Gate
State
0
Z
identity
|0>
1
Z
X
|1>
0
X
H
|+>
1
X
X then H
|->
Eliminated-state rule
Z basis outcome 0 eliminates |1>; Z basis outcome 1 eliminates |0>. X basis outcome 0 eliminates |->; X basis outcome 1 eliminates |+>. Verification is based on contradictions against this stored evidence.
Basic QDS: mismatches == 0. Teleportation QDS: observed mismatch rate <= acceptance threshold s_a.
Quantum Digital Signature (QDS) threat detection
2/5

## Slide 3
Eavesdropping detection: measurement disturbance becomes evidence
Intercept-resend is modeled as Eve measuring the qubit mid-channel and forwarding a possibly disturbed state.
Intercept-resend attack path
1
Eve intercepts each qubit with probability p_intercept.
2
Eve randomly chooses Z or X measurement basis.
3
The qubit is measured into Eve's classical register.
4
If Eve used the wrong basis, measurement collapses and disturbs the state.
5
Bob/Charlie later observe elevated QBER or QDS contradictions.
Why full intercept-resend gives about 25% QBER
Among sifted BB84 positions, Bob kept only cases where his basis matched Alice. Eve still has a 50% chance of choosing the wrong basis. When she is wrong, Bob has a 50% chance of receiving the wrong bit.
0.5 wrong basis * 0.5 wrong bit = 0.25 QBER
Detection thresholds used in the project
Communication layer: PointToPointProtocol and SecurePointToPointProtocol flag Eve when qber > qber_threshold; default threshold is 0.15.
QDS detection engine: channel eavesdropping is classified when channel_qber > 0.11, returning EAVESDROPPING_TAMPERING.
Signature-evidence view: Eve disturbance also increases Bob/Charlie mismatch rates and may create verifier asymmetry.
Quantum Digital Signature (QDS) threat detection
3/5

## Slide 4
Teleportation-based QDS and statistical security model
Stage 5 extends prepare-and-measure QDS with Bell pairs, syndrome recording, Pauli correction, and threshold certificates.
Bell pair
Create EPR pair with H and CX.
>
Signature qubit
Alice prepares token state on q0.
>
Bell measurement
CX(q0,q1), H(q0), then syndrome bits m1,m2.
>
Pauli correction
m2 maps to X; m1 maps to Z.
>
Verification
Receiver measures recovered qubit and records eliminated states.
Acceptance hierarchy
e0 < s_a < s_v < p_forg_min
e0 = baseline channel error; s_a = acceptance threshold; s_v = verification/rejection threshold; p_forg_min defaults to 0.25.
Chernoff-Hoeffding certificates
P_forge <= exp(-2 * delta^2 * L)
P_FRR <= exp(-2 * delta^2 * L)
P_rep <= 2 * exp(-0.5 * (s_v - s_a)^2 * L)
The module reports a security level as -log2(P_forge), capped at 256 bits.
Quantum Digital Signature (QDS) threat detection
4/5

## Slide 5
End-to-end system: deterministic threat engine and deliverables
The implementation combines a simulator, adversarial channel, deterministic classifier, security math, and network telemetry.
Decision pipeline
Freshness
>
QBER
>
Contradictions
>
Asymmetry
>
Classify
Priority order: missing tokens -> replay -> impersonation -> channel_qber > 0.11 -> clean authentic -> dishonest verifier -> repudiation -> channel noise -> external forgery.
Socket-network demo
ChannelProxyNode : port 8000
AliceDaemon : port 8001
Bob / Charlie : ports 8002 and 8003
DetectorDaemon : port 8004
In socket mode, qubits are represented as [bit, basis] descriptors. Eve modifies descriptors to mirror circuit-level measurement disturbance.
Expected deliverables
QDS teleportation core
Adversary testbed
Deterministic threat engine
Security math module
Network visualizer / telemetry dashboard
Key limitation: this is a simulator, not a deployed quantum network. The eavesdropping model is intercept-resend and the socket demo passes classical descriptors rather than physical qubits.
Quantum Digital Signature (QDS) threat detection
5/5